## Slide 1: Embedded System Lecture 13: USB Device
Shuo-Han Chen (陳碩漢), shchen@csie.ntut.edu.tw
Hong-Yue Technology Research Building 334
R 09:10 - 12:00
Department of Computer Science and Information Engineering

## Slide 2
2
USB
Widespread use of USB in embedded space
HOST MODE:
  To connect Ethernet/Hub
  To connect Modem
  To connect mass storage devices DEVICE MODE
Acts as mass storage device
  USB Speakers
  USB serial device
  USB webcam

## Slide 3
3
Good Features of USB
Ease of use
Hot pluggable
Speed
Reliability
Power devices from the bus
Bus expansion using hub
USB On-The-Go

## Slide 4
4
Linux USB Device
Drivers for Linux systems with a USB device controller
  Typical example: digital cameras. You connect the device to a PC and see the camera as a USB storage device.
USB device controller driver
  Platform dependent. Supports the chip connecting to the USB bus.
USB gadget drivers, platform independent.
  Examples:
    Ethernet gadget: implements networking through USB
    Storage gadget: makes the host see a USB storage device
    Serial gadget: for terminal-type of communication.
See Documentation/DocBook/gadget/ in kernel sources.

## Slide 5
5
Linux USB Device
System call interface
USB host controller driver
User applications
USB host controller
USB device
USB core
USB device drivers
Linux Kernel
Users
Hardware
Kernel subsystems
Kernel subsystems
Other kernel subsystems

## Slide 6
6
USB Host Controller (1/2)
OHCI - Open Host Controller Interface
  Compaq's implementation adopted as a standard for USB 1.0 and 1.1 by the USB Implementers Forum (USB-IF)
  Also used for Firewire devices
UHCI - Universal Host Controller Interface
  Created by Intel, insisting that other implementers use it and pay royalties for it. Only VIA licensed UHCI, and others stuck to OHCI.

## Slide 7
7
USB Host Controller (2/2)
EHCI - Extended Host Controller Interface.
  For USB 2.0. The only one to support high-speed transfers.
  Each EHCI controller contains four virtual HCD implementations to support Full Speed and Low Speed devices.
xHCI - eXtensible Host Controller Interface
  Specification is also referred to as the USB 3.0 host controller specification
  Capable of interfacing with USB 1.x, 2.0, and 3.x compatible devices

## Slide 8
8
Linux USB basics
USB descriptors
  Operating system independent
  Described in the USB specification
Device - Represent the devices connected to the USB bus. Example: USB speaker with volume control buttons.
Configurations - Represent the state of the device. Examples: Active, Standby, Initialization
Interfaces - Logical devices. Examples: speaker, volume control buttons.
Endpoints - Unidirectional communication pipes. Either IN (device to computer) or OUT (computer to device).

## Slide 9
9
Endpoints
Control endpoints
  Used to configure the device, get information about it, send commands to it, retrieve status information.
  Simple, small data transfers.
  Every device has a control endpoint (endpoint 0), used to configure the device at insertion time.
  The USB protocol guarantees that the corresponding data transfers will always have enough (reserved) bandwidth.

## Slide 10
10
Endpoints
Interrupt endpoints
  Transfer small amounts of data at a fixed rate each time the hosts asks the device for data.
  Guaranteed, reserved bandwidth.
  For devices requiring guaranteed response time, such as USB mice and keyboards.
  Note: different than hardware interrupts. Require constant polling from the host.

## Slide 11
11
Endpoints
Bulk endpoints
  Large sporadic data transfers using all remaining available bandwidth.
  No guarantee on bandwidth or latency.
  Guarantee that no data is lost.
  Typically used for printers, storage or network devices.

## Slide 12
12
Endpoints
Isochronous endpoints
  Also for large amounts of data.
  Guaranteed speed (often but not necessarily as fast as possible).
  No guarantee that all data makes it through.
  Used by real-time data transfers (typically audio and video).

## Slide 13
13
The usb_endpoint_descriptor structure (1)
The usb_endpoint_descriptor structure contains all the USB-specific data announced by the device itself.
Here are useful fields for driver writers:
  __u8 bEndpointAddress
    USB address of the endpoint.
    It also includes the direction of the endpoint.
    You can use the USB_ENDPOINT_DIR_MASK bitmask to tell whether this is a USB_DIR_IN or USB_DIR_OUT endpoint.
    Example:
  if ((endpoint->desc.bEndpointAddress & USB_ENDPOINT_DIR_MASK) == USB_DIR_IN)

## Slide 14
14
The usb_endpoint_descriptor structure (2)
  __u8 bmAttributes: The type of the endpoint. You can use the USB_ENDPOINT_XFERTYPE_MASK bitmask to tell whether the type is USB_ENDPOINT_XFER_ISOC, USB_ENDPOINT_XFER_BULK, USB_ENDPOINT_XFER_INT or USB_ENDPOINT_XFER_CONTROL.
  __u8 wMaxPacketSize: Maximum size in bytes that the endpoint can handle. Note that if greater sizes are used, data will be split in wMaxPacketSize chunks.
  __u8 bInterval: For interrupt endpoints, device polling interval (in milliseconds).
  Note that the above names do not follow Linux coding standards. The Linux USB implementation kept the original name from the USB specification (http://www.usb.org/developers/docs/).

## Slide 15
15
Interface
Each interface encapsulates a single high-level function (USB logical connection).
  Example (USB webcam): video stream, audio stream, keyboard (control buttons).
One driver is needed for each interface!
Alternate settings: each USB interface may have different parameter settings.
  Example: different bandwidth settings for an audio interface. The initial state is in the first setting, (number 0).
  Alternate settings are often used to control the use of periodic endpoints, such as by having different endpoints use different amounts of reserved USB bandwidth.
  All standards-compliant USB devices that use isochronous endpoints will use them in non-default settings.

## Slide 16
16
The usb_interface structure (1)
USB interfaces are represented by the usb_interface structure. It is what the USB core passes to USB drivers.
struct usb_host_interface *altsetting;
  List of alternate settings that may be selected for this interface, in no particular order.
  The usb_host_interface structure for each alternate setting allows to access the usb_endpoint_descriptor structure for each of its endpoints: interface->alsetting[i]->endpoint[j]->desc
unsigned int num_altsetting;
  The number of alternate settings.

## Slide 17
17
The usb_interface structure (2)
  struct usb_host_interface *cur_altsetting; The currently active alternate setting.
  int minor; Minor number this interface is bound to. (for drivers using usb_register_dev(), described later).
  Other fields in the structure shouldn't be needed by USB drivers

## Slide 18
18
Configurations
Interfaces are bundled into configurations.
Configurations represent the state of the device. Examples: Active, Standby, Initialization
Configurations are described with the usb_host_config structure.
However, drivers do not need to access this structure.

## Slide 19
19
Device
Devices are represented by the usb_device structure.
We will see later that several USB API functions need such a structure.
Many drivers use the interface_to_usbdev() function to access their usb_device structure from the usb_interface structure they are given by the USB core.

## Slide 20
20
USB Device Overview
Device USB webcam
Configuration
Configuration Active
Interface Audio
endpoint control
endpoint input
Interface Video
endpoint control
endpoint input
Configuration
Configuration Standby
Interface Audio
endpoint control
endpoint input
Interface Video
endpoint control
endpoint input

## Slide 21
21
USB devices - Summary
Hierarchy: device -> configurations -> interfaces -> endpoints
4 different types of endpoints
  control: device control, accessing information, small transfers. Guaranteed bandwidth.
  interrupt (keyboards, mice...): data transfer at a fixed rate. Guaranteed bandwidth.
  bulk (storage, network, printers...): use all remaining bandwidth. No bandwidth or latency guarantee.
  isochronous (audio, video...): guaranteed speed. Possible data loss.

## Slide 22
22
Linux USB - User-space Representation
usbview
http://usbview.sourceforge.net Graphical display of the contents of /proc/bus/usb/devices.

## Slide 23
23
USB Gadget Drivers
http://www.linux-usb.org/usbtree
Also displays information from /proc/bus/usb/devices:
  > usbtree \/: Bus 04.Port 1: Dev 1, Class=root_hub, Driver=ehci_hcd/6p, 480M /: Bus 03.Port 1: Dev 1, Class=root_hub, Driver=uhci_hcd/2p, 12M /: Bus 02.Port 1: Dev 1, Class=root_hub, Driver=uhci_hcd/2p, 12M |__ Port 1: Dev 7, If 0, Class=HID, Driver=usbhid, 1.5M /: Bus 01.Port 1: Dev 1, Class=root_hub, Driver=uhci_hcd/2p, 12M

## Slide 24
24
Linux USB Communication
USB Request Blocks
  Any communication between the host and device is done asynchronously using USB Request Blocks (urbs).
  They are similar to packets in network communications.
  Every endpoint can handle a queue of urbs.
  Every urb has a completion handler.
  A driver may allocate many urbs for a single endpoint, or reuse the same urb for different endpoints.
See Documentation/usb/URB.txt in kernel sources.

## Slide 25
25
Urb Life
The lifecycle of an urb
Creation
Assigned to an endpoint
Submitted to the USB core
Transfered to the device
Deletion
can be reused?
Notification at transfer completion
yes
no
Device driver
USB core (controller driver)

## Slide 26
26
The urb structure (1)
Fields of the urb structure useful to USB device drivers:
  struct usb_device *dev; Device the urb is sent to.
  unsigned int pipe; Information about the endpoint in the target device.
  int status; Transfer status.
  unsigned int transfer_flags; Instructions for handling the urb.
  void * transfer_buffer; Buffer storing transferred data. Must be created with kmalloc()!

## Slide 27
27
The urb structure (2)
  dma_addr_t transfer_dma; Data transfer buffer when DMA is used.
  int transfer_buffer_length; Transfer buffer length.
  int actual_length; Actual length of data received or sent by the urb.
  usb_complete_t complete; Completion handler called when the transfer is complete.
  void *context; Data blob which can be used in the completion handler.
  unsigned char *setup_packet; (control urbs) Setup packet transferred before the data in the transfer buffer.
  dma_addr_t setup_dma; (control urbs) Same, but when the setup packet is transferred with DMA.

## Slide 28
28
The urb structure (3)
  int interval; (isochronous and interrupt urbs) Urb polling interval.
  int error_count; (isochronous urbs) Number of isochronous transfers which reported an error.
  int start_frame; (isochronous urbs) Sets or returns the initial frame number to use.
  int number_of_packets; (isochronous urbs) Number of isochronous transfer buffers to use.
  struct usb_iso_packet_descriptor (isochronous urbs) iso_frame_desc[0]; Allows a single urb to define multiple isochronous transfers at once.

## Slide 29
29
Creating Pipes
pipe : endpoint information
Create the “pipe” value using values from the appropriate endpoint descriptor
Functions used to initialize the pipe field of the urb structure:
  Control pipes usb_sndctrlpipe(), usb_rcvctrlpipe()
  Bulk pipes usb_sndbulkpipe(), usb_rcvbulkpipe()
  Interrupt pipes usb_sndintpipe(), usb_rcvintpipe()
  Isochronous pipes usb_sndisocpipe(), usb_rcvisocpipe()
  Prototype
unsigned int usb_[snd/rcv][ctrl/bulk/int/isoc]pipe( struct usb_device *dev, unsigned int endpoint);
send (out)
receive (in)

## Slide 30
30
Creating urbs
urb structures must always be allocated with the usb_alloc_urb() function.
That's needed for reference counting used by the USB core.
  #include <linux/usb.h>
  struct urb *usb_alloc_urb( int iso_packets, // Number of isochronous // packets the urb should contain. // 0 for other transfer types gfp_t mem_flags); // Standard kmalloc() flags
Check that it didn't return NULL (allocation failed)!
Typical example: urb = usb_alloc_urb(0, GFP_KERNEL);

## Slide 31
31
Freeing urbs
Similarly, you have to use a dedicated function to release urbs:
void usb_free_urb(struct urb *urb);

## Slide 32
32
USB Request Blocks - Summary
Basic data structure used in any USB communication.
Implemented by the struct urb type.
Must be created with the usb_alloc_urb() function. Shouldn't be allocated statically or with kmalloc().
Must be deleted with usb_free_urb()

## Slide 33
33
Initializing Interrupt urbs
void usb_fill_int_urb ( struct urb *urb, // urb to be initialized struct usb_device *dev, // device to send the urb to unsigned int pipe, // pipe (endpoint and device specific) void *transfer_buffer, // transfer buffer int buffer_length, // transfer buffer size usb_complete_t complete, // completion handler void *context, // context (for handler) int interval // Scheduling interval (see next page) );
This doesn't prevent you from making more changes to the urb fields before urb submission.
The transfer_flags field needs to be set by the driver.

## Slide 34
34
urb Scheduling Interval
For interrupt and isochronous transfers
  Low-Speed and Full-Speed devices: the interval unit is frames (ms)
  Hi-Speed devices: the interval unit is microframes (1/8 ms)

## Slide 35
35
Initializing Bulk urbs
Same parameters as in usb_fill_int_urb(), except that there is no interval parameter.
void usb_fill_bulk_urb ( struct urb *urb, // urb to be initialized struct usb_device *dev, // device to send the urb to unsigned int pipe, // pipe (endpoint and device specific) void *transfer_buffer, // transfer buffer int buffer_length, // transfer buffer size usb_complete_t complete, // completion handler void *context, // context (for handler) );

## Slide 36
36
Initializing Control urbs
Same parameters as in usb_fill_bulk_urb(), except that there is a setup_packet parameter.
Note that many drivers use the usb_control_msg() function instead (explained later).
void usb_fill_control_urb ( struct urb *urb, // urb to be initialized struct usb_device *dev, // device to send the urb to unsigned int pipe, // pipe (endpoint and device specific) unsigned char *setup_packet, // setup packet data void *transfer_buffer, // transfer buffer int buffer_length, // transfer buffer size usb_complete_t complete, // completion handler void *context, // context (for handler) );

## Slide 37
37
Initializing Isochronous urbs
No helper function. Has to be done manually by the driver.
drivers/media/video/usbvideo/usbvideo.c example
for (i=0; i < USBVIDEO_NUMSBUF; i++) {
int j, k;
struct urb *urb = uvd->sbuf[i].urb;
urb->dev = dev;
urb->context = uvd;
urb->pipe = usb_rcvisocpipe(dev, uvd->video_endp);
urb->interval = 1;
urb->transfer_flags = URB_ISO_ASAP;
urb->transfer_buffer = uvd->sbuf[i].data;
urb->complete = usbvideo_IsocIrq;
urb->number_of_packets = FRAMES_PER_DESC;
urb->transfer_buffer_length = uvd->iso_packet_len * FRAMES_PER_DESC;
for (j=k=0; j < FRAMES_PER_DESC; j++, k += uvd->iso_packet_len) {
urb->iso_frame_desc[j].offset = k;
urb->iso_frame_desc[j].length = uvd->iso_packet_len;
}
}

## Slide 38
38
Allocating DMA buffers (1)
You can use the usb_buffer_alloc() function to allocate a DMA consistent buffer:
void *usb_buffer_alloc ( struct usb_device *dev, // device size_t size, // buffer size gfp_t mem_flags, // kmalloc() flags dma_addr_t *dma // (output) DMA address of the buffer );
Example:
buf = usb_buffer_alloc(dev->udev, count, GFP_KERNEL, &urb->transfer_dma);

## Slide 39
39
Allocating DMA buffers (2)
To use these buffers, use the URB_NO_TRANSFER_DMA_MAP or URB_NO_SETUP_DMA_MAP settings for urb->transfer_flags to indicate that urb->transfer_dma or urb->setup_dma are valid on submit.
Examples:
urb->transfer_flags |= URB_NO_TRANSFER_DMA_MAP; u->transfer_flags |= URB_NO_SETUP_DMA_MAP;
Freeing these buffers:
void usb_buffer_free ( struct usb_device *dev, // device size_t size, // buffer size void *addr, // CPU address of buffer dma_addr_t dma // DMA address of buffer );

## Slide 40
40
Submitting urbs
After creating and initializing the urb
int usb_submit_urb( struct urb *urb, // urb to submit int mem_flags); // kmalloc() flags
mem_flags is used for internal allocations performed by usb_submit_urb().
Settings that should be used:
  GFP_ATOMIC: called from code which cannot sleep: a urb completion handler, hard or soft interrupts. Or called when the caller holds a spinlock.
  GPF_NOIO: in some cases when block storage is used.
  GFP_KERNEL: in other cases.

## Slide 41
41
usb_submit_urb return values
usb_submit_urb() immediately returns:
  0: Request queued
  -ENOMEM: Out of memory
  -ENODEV: Unplugged device
  -EPIPE: Stalled endpoint
  -EAGAIN: Too many queued ISO transfers
  -EFBIG: Too many requested ISO frames
  -EINVAL: Invalid INT interval More than one packet for INT

## Slide 42
42
Canceling urbs Asynchronously
To cancel a submitted urb without waiting
  int usb_unlink_urb(struct urb *urb);
  Success: returns –EINPROGRESS
  Failure: any other return value. It can happen:
    When the urb was never submitted
    When the has already been unlinked
    When the hardware is done with the urb, even if the completion handler hasn't been called yet.
  The corresponding completion handlers will still be run and will see urb->status == -ECONNRESET.

## Slide 43
43
Canceling urbs Synchronously
To cancel an urb and wait for all completion handlers to complete
This guarantees that the urb is totally idle and can be reused.
void usb_kill_urb(struct urb *urb);
  Typically used in a disconnect() callback or close() function.
  Caution: this routine mustn't be called in situations which can not sleep: in interrupt context, in a completion handler, or when holding a spinlock.
See comments in drivers/usb/core/urb.c in kernel sources for useful details.

## Slide 44
44
Initializing and Submitting urbs - Summary
urb structure fields can be initialized with helper functions usb_fill_int_urb(), usb_fill_bulk_urb() , usb_fill_control_urb()
Isochronous urbs have to be initialized by hand.
The transfer_flags field must be initialized manually by each driver.
Use the usb_submit_urb() function to queue urbs.
Submitted urbs can be canceled using usb_unlink_urb() (asynchronous) or usb_kill_urb() (synchronous).

## Slide 45
45
Completion Handlers
When is the completion handler called?
The completion handler is called in interrupt context, in only 3 situations. Check the error value in urb->status.
  After the data transfer successfully completed. urb->status == 0
  Error(s) happened during the transfer.
  The urb was unlinked by the USB core.
urb->status should only be checked from the completion handler!

## Slide 46
46
Transfer Status (1)
Described in Documentation/usb/error-codes.txt
The urb is no longer “linked” in the system
-ECONNRESET The urb was unlinked by usb_unlink_urb().
-ENOENT The urb was stopped by usb_kill_urb().
-ESHUTDOWN Error in from the host controller driver. The device was disconnected from the system, the controller was disabled, or the configuration was changed while the urb was sent.
-ENODEV Device removed. Often preceded by a burst of other errors, since the hub driver doesn't detect device removal events immediately.

## Slide 47
47
Transfer Status (2)
Typical hardware problems with the cable or the device (including its firmware)
-EPROTO Bitstuff error, no response packet received in time by the hardware, or unknown USB error.
-EILSEQ CRC error, no response packet received in time, or unknown USB error.
-EOVERFLOW The amount of data returned by the endpoint was greater than either the max packet size of the endpoint or the remaining buffer size. "Babble".

## Slide 48
48
Transfer Status (3)
-EINPROGRESS Urb not completed yet. Your driver should never get this value.
-ETIMEDOUT Usually reported by synchronous USB message functions when the specified timeout was exceed.
-EPIPE Endpoint stalled. For non-control endpoints, reset this status with usb_clear_halt().
-ECOMM During an IN transfer, the host controller received data from an endpoint faster than it could be written to system memory.

## Slide 49
49
Transfer Status (4)
-ENOSR During an OUT transfer, the host controller could not retrieve data from system memory fast enough to keep up with the USB data rate.
-EREMOTEIO The data read from the endpoint did not fill the specified buffer, and URB_SHORT_NOT_OK was set in urb->transfer_flags.
-EXDEV Isochronous transfer only partially completed. Look at individual frame status for details.
-EINVAL Typically happens with an incorrect urb structure field or usb_submit_urb() function parameter.

## Slide 50
50
Completion Handler Implementation
Prototype:
void (*usb_complete_t)( struct urb *, // The completed urb struct pt_regs * // Register values at the time // of the corresponding interrupt (if any) );
Remember you are in interrupt context:
Do not execute call which may sleep (use GFP_ATOMIC, etc.).
Complete as quickly as possible. Schedule remaining work in a tasklet if needed.

## Slide 51
51
Supported Devices
What Devices does the Driver Support?
Or what driver supports a given device?
  Information needed by user-space, to find the right driver to load or remove after a USB hotplug event.
  Information needed by the driver, to call the right probe() and disconnect() driver functions (see later).
Such information is declared in a usb_device_id structure by the driver init() function.

## Slide 52
52
The usb_device_id Structure (1)
Defined according to USB specifications and described in include/linux/mod_devicetable.h.
__u16 match_flags Bitmask defining which fields in the structure are to be matched against. Usually set with helper functions described later.
__u16 idVendor, idProduct USB vendor and product id, assigned by the USB-IF.
__u16 bcdDevice_lo, bcdDevice_hi Product version range supported by the driver, expressed in binary-coded decimal (BCD) form.

## Slide 53
53
The usb_device_id Structure (2)
__u8 bDeviceClass, bDeviceSubClass, bDeviceProtocol Class, subclass and protocol of the device. Numbers assigned by the USB-IF. Products may choose to implement classes, or be vendor-specific. Device classes specify the behavior of all the interfaces on a device.
__u8 bInterfaceClass, bInterfaceSubclass, bInterfaceProtocol Class, subclass and protocol of the individual interface. Numbers assigned by the USB-IF. Interface classes only specify the behavior of a given interface. Other interfaces may support other classes.
kernel_ulong_t driver_info

## Slide 54
54
The usb_device_id Structure (3)
kernel_ulong_t driver_info Holds information used by the driver. Usually it holds a pointer to a descriptor understood by the driver, or perhaps device flags. This field is useful to differentiate different devices from each other in the probe() function.

## Slide 55
55
Declaring Supported Devices (1)
USB_DEVICE(vendor, product)
  Creates a usb_device_id structure which can be used to match only the specified vendor and product ids.
  Used by most drivers for non-standard devices.
USB_DEVICE_VER(vendor, product, lo, hi)
  Similar, but only for a given version range.
  Only used 11 times throughout Linux 2.6.18!

## Slide 56
56
Declaring Supported Devices (2)
USB_DEVICE_INFO (class, subclass, protocol)
  Matches a specific class of USB devices
USB_INTERFACE_INFO (class, subclass, protocol)
  Matches a specific class of USB interfaces.
The above 2 macros are only used in the implementations of standard device and interface classes.

## Slide 57
57
Declaring Supported Devices (3)
Created usb_device_id structures are declared with the MODULE_DEVICE_TABLE() macro as in the below example:
/* Example from drivers/usb/net/catc.c */ static struct usb_device_id catc_id_table [] = { { USB_DEVICE(0x0423, 0xa) }, /* CATC Netmate, Belkin F5U011 */ { USB_DEVICE(0x0423, 0xc) }, /* CATC Netmate II, Belkin F5U111 */ { USB_DEVICE(0x08d1, 0x1) }, /* smartBridges smartNIC */ { } /* Terminating entry */ };
MODULE_DEVICE_TABLE(usb, catc_id_table);
Note that MODULE_DEVICE_TABLE() is also used with other subsystems: pci, pcmcia, serio, isapnp, input...

## Slide 58
58
Supported Devices - Summary
Drivers need to announce the devices they support in usb_device_id structures.
Needed for user space to know which module to (un)load, and for the kernel which driver code to execute, when a device is inserted or removed.
Most drivers use USB_DEVICE() to create the structures.
These structures are then registered with MODULE_DEVICE_TABLE(usb, xxx).

## Slide 59
59
Registering a USB Driver
USB drivers must define a usb_driver structure:
  const char *name Unique driver name. Usually be set to the module name.
  const struct usb_device_id *id_table; The table already declared with MODULE_DEVICE_TABLE().
  int (*probe) (struct usb_interface *intf, const struct usb_device_id *id); Probe callback (detailed later).
  void (*disconnect) (struct usb_interface *intf); Disconnect callback (detailed later).

## Slide 60
60
Registering a USB Driver
Optional usb_driver structure fields
  int (*suspend) (struct usb_interface *intf, pm_message_t message); int (*resume) (struct usb_interface *intf); Power management: callbacks called before and after the USB core suspends and resumes the device.
  void (*pre_reset) (struct usb_interface *intf); void (*post_reset) (struct usb_interface *intf); Called by usb_reset_composite_device() before and after it performs a USB port reset.

## Slide 61
61
Driver Registration
Use usb_register() to register your driver. Example:
/* Example from drivers/usb/input/mtouchusb.c */
static struct usb_driver mtouchusb_driver = { .name = "mtouchusb", .probe = mtouchusb_probe, .disconnect = mtouchusb_disconnect, .id_table = mtouchusb_devices, }; static int __init mtouchusb_init(void) { dbg("%s - called", __FUNCTION__); return usb_register(&mtouchusb_driver); }

## Slide 62
62
Driver Unregistration
Use usb_deregister() to register your driver. Example:
/* Example from drivers/usb/input/mtouchusb.c */
static void __exit mtouchusb_cleanup(void)
{ dbg("%s - called", __FUNCTION__); usb_deregister(&mtouchusb_driver); }

## Slide 63
63
probe() and disconnect() Functions
The probe() function is called by the USB core to see if the driver is willing to manage a particular interface on a device.
The driver should then make checks on the information passed to it about the device.
If it decides to manage the interface, the probe() function will return 0. Otherwise, it will return a negative value.
The disconnect() function is called by the USB core when a driver should no longer control the device (even if the driver is still loaded), and should do some clean-up.

## Slide 64
64
Context: USB hub kernel thread
The probe() and disconnect() callbacks are called in the context of the USB hub kernel thread.
So, it is legal to call functions which may sleep in these functions.
However, all addition and removal of devices is managed by this single thread.
Most of the probe function work should indeed be done when the device is actually opened by a user. This way, this doesn't impact the performance of the kernel thread in managing other devices.

## Slide 65
65
usb_set_intfdata() / usb_get_intfdata()
static inline void usb_set_intfdata ( struct usb_interface *intf, void *data);
Function used in probe() functions to attach collected device data to an interface. Any pointer will do!
Useful to store information for each device supported by a driver, without having to keep a static data array.
The usb_get_intfdata() function is typically used in the device open functions to retrieve the data.
Stored data need to be freed in disconnect() functions: usb_set_intfdata(interface, NULL);
Plenty of examples are available in the kernel sources.

## Slide 66
66
Transfers without URBs
The kernel provides two usb_bulk_msg() and usb_control_msg() helper functions that make it possible to transfer simple bulk and control messages, without having to:
  Create or reuse an urb structure,
  Initialize it,
  Submit it,
  And wait for its completion handler.

## Slide 67
67
Transfers without URBs - Constraints
These functions are synchronous and will make your code sleep. You must not call them from interrupt context or with a spinlock held.
You cannot cancel your requests, as you have no handle on the URB used internally. Make sure your disconnect() function can wait for these functions to complete.
See the kernel sources for examples using these functions!

## Slide 68
68
USB Device Drivers - Summary
Module loading
Declare supported devices (interfaces).
Bind them to probe() and disconnect() functions.
Supported devices are found
probe() functions for matching interface drivers are called.
They record interface information and register resources or services.
Devices are opened
This calls data access functions registered by the driver.
URBs are initialized.
Once the transfers are over, completion functions are called. Data are copied from/to user-space.
Devices are removed
The disconnect() functions are called.
The drivers may be unloaded.

## Slide 69
That’s all for today.
Notes: Thank you for listening. Now, I would like to end today’s talk by the Q & A time.